## Slide 1: GeantV – From CPU to accelerators
Philippe Canal (FNAL) for the GeantV development team
G.Amadio (UNESP), Ananya (CERN), J.Apostolakis (CERN) , A.Arora (CERN), M.Bandieramonte (CERN), A.Bhattacharyya (BARC), C.Bianchini (UNESP), R.Brun (CERN), Ph.Canal (FNAL), F.Carminati (CERN), L.Duhem (intel), D.Elvira (FNAL), A.Gheata (CERN), M.Gheata (CERN), I.Goulas (CERN), R.Iope (UNESP), S.Y.Jun (FNAL), G.Lima (FNAL), A.Mohanty (BARC), T.Nikitina (CERN), M.Novak (CERN), W.Pokorski (CERN), A.Ribon (CERN), R.Sehgal (BARC), O.Shadura (CERN), S.Vallecorsa (CERN), S.Wenzel (CERN), Y.Zhang (CERN)

## Slide 2: Outline
GeantVectorized – an introduction
  The problem
  Existing solutions
  Challenges, ideas, goals
Main components and performance
  Design and infrastructure
  Vectorization: overheads vs. gains
  Geometry library
  Physics processes
Performance benchmarks
Results, milestones, plans

## Slide 3: The problem
Detailed simulation of subatomic particle transport and interactions in detector geometries
Using state of the art physics models, propagation in electromagnetic fields in geometries having complexities of millions of parts
Heavy computation requirements, massively CPU-bound, seeking organically HPC solutions…
The LHC uses more than 50% of its distributed GRID power for detector simulations (~250.000 CPU years equivalent so far)
http://atlas.ch

## Slide 4: The Geant4 Simulation Toolkit
An OO C++ software toolkit to simulate the passage of particles through matter and EM fields. The user writes a “G4 Application”:
  Experimental setup (detector geometry & materials, magnetic field)
  Primary particles that hit the detector
  Set of physics models to simulate interaction of particles with matter
  User scoring and signal-generation
Primary particles are “transported” within the detector using:
  The equations of motion in EM fields
  Cross sections of all possible physics processes for each particle
  Process final states information to generate secondary particles which are sequentially transported and result in a “shower”
Output is a collection of “particle trajectories” and “simulated hits” with position, time, energy deposited in detector volumes

## Slide 5: Geant4 Geometry
The user constructs a detector within a “world volume” as a collection of placed volumes of different shapes, materials
  G4VSolid: shape and size
  G4LogicalVolume: material, sensitivity, magnetic field
  G4VPhysical Volume: position, rotation
Materials could be elements, isotopes, mixture (i.e. air)

## Slide 6: Geant4 Geometry
A large collection of solids are defined in Geant4:
G4Cons
G4Tubs
G4Polycone, G4 Polyhedra, G4Hype, G4TwistedTubs, G4TwistedTrap
Also Boolean solids such us:

## Slide 7: Geant4 Primary Event
A “Run” is a collection of simulated “Events”
A simulated event is defined by a collection of incoming “primary particles” that come from a:
  pp, ppbar, e+e-, ep collision
  particle beam
Primary particles are fed to the Geant4 application through a:
  G4ParticleGun in the case of a beam
  G4HEPEvtInterface (HEPMC) to event generators such as PYTHIA
G4 particles (primaries and secondaries) are described by:
  G4ParticleDefinition (name, mass, spin, etc)
  G4VDynamicParticle (adds energy, momentum, polarization, etc)

## Slide 8: Geant4 Transportation
The G4Track information is updated after every G4Step
  A G4Step is a step in the particle (track) propagation
  The user defines a maximum step length but steps also end when a physics process is invoked and at volume boundaries
A G4Track also includes the info for transporting the particle through the detector  in G4 we typically use Particle = Track
T2-T8 (secondary tracks)
Tracking follows “last in first out” rule:
T1->T4->T3->T6->T7 ->T5->T8->T2

## Slide 9: Geant4 Magnetic Field
Particle propagated in EM field by integration of equation of motion using the Runge-Kutta method (others also available)
  Curved path broken into linear chord segments to minimize the sagitta (maximum chord-trajectory distance)
  Chords used to interrogate navigator on whether the track has crossed a volume boundary
  miss distance parameter used to tune volume intersection accuracy
G4 supports user defined, uniform, and non-uniform (static or time dependent) magnetic fields

## Slide 10: Geant4 Physics
Geant4 does not provide “one size fits all” modeling of interaction of each particle type with matter but instead:
  A set of models for physics processes which include the cross sections and final state information for each particle type
  The process categories are electromagnetic, hadronic, decay, optical, photolepton_hadron, parameterization, transportation
  Three kinds of process actions: AtRest (decay, annihilation), AlongStep (continuous interactions like ionization), PostStep (point-like interactions like decay in flight, EM, hadronic)
Processes are defined for both primary and secondary particles
  Particles tracked down to zero kinematic energy
  Production cuts on secondary particles set to a default of 1 mm, secondaries with Ekin < ETh to travel 1 mm are stopped

## Slide 11: Geant4 EM Physics
EM processes for g, e±
Particle | Process | G4Process
Photons | Gamma Conversion in e± | G4GammaConversion
 | Compton scattering | G4ComptonScattering
 | Photoelectric effect | G4PhotoElectricEffect
 | Rayleigh scattering | G4RayleighScattering
e± | Ionisation | G4eIonisation
 | Bremsstrahlung | G4eBremsstrahlung
 | Multiple scattering | G4eMultipleScattering
e+ | Annihilation | G4eplusAnnihilation
Particle | Process | G4Process
m± | Ionisation | G4MuIonisation
 | Bremsstrahlung | G4MuBremsstrahlung
 | Multiple scattering | G4MuMultipleScattering
 | e± pair production | G4MuPairProduction
EM processes for m±

## Slide 12: Geant4 Hadronic Physics
Geant4 hadronic physics consists of data-driven, parameterised and theory-driven models
  Three energy regimes: <100 MeV, 100 MeV-10 GeV, >10 GeV
  Several models available within each regime
  Processes: stopping, capture, elastic, inelastic, fission

## Slide 13: Geant4 Physics Lists
Geant4 provides a set of “physics lists” or combinations of models best suited to different application areas such as:
  High energy physics, LHC neutron fluxes, shielding, medical
  Different models are better suited to some energy ranges, or materials involved
HEP example: “QGSP_BERT” physics list
Bertini model: generates the final state for hadron inelastic scattering by simulating the intra-nuclear cascade
QGS model: two or more strings stretched between the quark or gluons within the hadrons

## Slide 14
Event level Parallelism
  Each thread processes one full event exclusively
  Part of Geant4 since release 10.0, Dec. 2013
Preliminary, Courtesy of A.Dotti, SLAC
Demonstrates
  Linear scaling of throughput with number of threads
Large savings in memory: 40MB extra memory per thread
Geant4 Multi-threading

## Slide 15: GeantV: (familiar) motivations
transistors
clock
power
ILP
10-1
1
10
102
103
104
105
106
70
75
80
85
90
95
00
05
10
107
Performance of our code scales with clock cycle (hence is stagnant!)
Needs will increase more than tenfold and the budget will be constant at best
HEP code needs to exploit new architectures and to team with other disciplines to share the optimization effort
  Data & instruction locality and vectorisation
Portability, better physics and optimization will be the targets
Simulation can lead the way to show how to exploit today's CPU's resources more effectively in complex applications
Seeking ways to write code portable between CPU with vector units or not and accelerators (GPU, Xeon Phi)

## Slide 16: The Eight dimensions
The “dimensions of performance”
  Vectors
  Instruction Pipelining
  Instruction Level Parallelism (ILP)
  Hardware threading
  Clock frequency
  Multi-core
  Multi-socket
  Multi-node
Possibly running different
jobs as we do now is the
best solution
}
Gain in memory footprint
and time-to-solution
but not in throughput
Very little gain to be expected and no action to be taken
Micro-parallelism: gain in throughput and
in time-to-solution
Expected limits on performance scaling |  |  | 
 | SIMD | ILP | HW THREADS
IDEAL | 8 | 4 | 1.35
OPTIMISED | 6 | 1.57 | 1.25
HEP Code | 1 | 0.8 | 1.25
Expected limits on performance scaling (multiplied) |  |  | 
 | SIMD | ILP | HW THREADS
IDEAL | 8 | 32 | 43.2
OPTIMISED | 6 | 9.43 | 11.79
HEP Code | 1 | 0.8 | 1
OpenLab@CHEP12

## Slide 17: Why Reengineer Geant?
Geant4 is THE simulation toolkit for HEP
Simulation is largely experiment independent and improvement there benefits directly all experiments and even other fields (Medical, etc.)
Geant4 is the largest (50%) single consumer of the WLCG cycles.

## Slide 18: Why not Geant4+?
Extensive prototyping and analysis has convinced us that “vectorisation” of Geant4 was not achievable without a major rewrite of the code
  No hotspots (!)
  Virtual table structure very deep and complex (1990’s style)
  Codebase very large and non-homogeneous
  Auto-vectorization can only have small and very localized effect
No criticism, but even the best things age (born 1994)

## Slide 19: Geant4 Profiling Example: Call Graph
valgrind / gprof2dot / graphviz
Small and Smaller boxes!!
Geant4 example B1 with 100 protons

## Slide 20: Geant4 Profiling Example: Call Map
valgrind / kcachegrind
No easy to address hotspots

## Slide 21: What do we want to do?
Develop an all-particle transport simulation software with
  Geant4 physics models
  A performance between 2 and 5 times greater than Geant4
  Full simulation and various options for fast simulation
  Portable on different architectures, including accelerators (GPUs and Xeon Phi’s)
Understand the limiting factors for a one-order-of-magnitude (10x) improvement

## Slide 22: The ideas
Transport particles in groups (vectors) rather than one by one
  Group particles by geometry volume or same physics
  No free lunch: data gathering overheads < vector gains
Dispatch SoA to functions with vector signatures
  Use backends to abstract interface: vector, scalar
  Use backends to insulate technology/library: Vc, Cilk+, VecMic, …
Redesign the library and workflow to target fine grain parallelism
  CPU, GPU, Phi, Atom, …
  Aim for a 3x-5x faster code, understand hard limits for more
template<class Backend>
Backend::double_t
common_distance_function( Backend::double_t input )
{
// Single kernel algorithm using Backend types
}
struct VectorVcBackend
{
typedef Vc::double_v double_t;
typedef Vc::double_m bool_t;
static const boolIsScalar=false;
static const bool IsSIMD=true;
};
// Functions operating with backend types
distance( vector_type &);
distance( double &);
struct ScalarBackend
{
typedef double double_t;
typedef bool bool_t;
static const bool IsScalar=true;
static const bool IsSIMD=false;
};
// Functions operating with backend types
Scalar interface
Vector interface
code.compeng.uni-frankfurt.de/projects/vc

## Slide 23: HEP transport is mostly local !
ATLAS volumes sorted by transport time. The same behavior is observed for most HEP geometries.
50 per cent of the time spent in 50/7100 volumes
Locality not exploited by the classical transport
Existing code very inefficient (0.6-0.8 IPC)
Cache misses due to fragmented code

## Slide 24
Scheduler
Geometry navigator
Geometry algorithms
Physics
Basket of tracks
Basket of tracks
x-sections
Reactions
Dispatching
MIMD
SIMD
The initial ideas sounded easy

## Slide 25: “Basketised” transport
Deal with particles in parallel
Output buffer(s)
Particles are transported per thread and put in output buffers
A dispatcher thread puts particles back into transport buffers
Everything happens asynchronously and in parallel
The challenge is to minimise locks
Keep long vectors
Avoid memory explosion

## Slide 26
Scheduler
Outputs
Geometry
Filters
Baskets
(Fast)Physics
Filters
Stepper
Input queue
Vector
stepper
Step sampling
Filter neutrals
(Field) Propagator
Step limiter
reshuffle
VecGeom
navigator
Full geometry
Simplified geometry
Physics sampler
Phys. Process
post-step
Secondaries
TO SCHEDULER
Vol1
Vol2
Vol3
Voln
e+/e-
γ
GeantV
Coproc. broker
105 baskets/sec

## Slide 27
Scheduler
Outputs
Geometry
Filters
Baskets
(Fast)Physics
Filters
Stepper
Input queue
Vector
stepper
Step sampling
Filter neutrals
(Field) Propagator
Step limiter
reshuffle
VecGeom
navigator
Full geometry
Simplified geometry
Physics sampler
Phys. Process
post-step
Secondaries
TO SCHEDULER
Vol1
Vol2
Vol3
Voln
e+/e-
γ
GeantV
Coproc. broker
105 baskets/sec

## Slide 28: Challenges
Overhead from reshuffling particle lists should not offset SIMD gains
Exploit the hardware at its best, while maintaining portability
Test from the onset on a “large” setup (LHC-like detector)
  Toy models tell us very little – complexity is the problem
Scheduler
CPU
GPU
Phi
XXX
Atom

## Slide 29: Yardstick: CMS With Tabulated Physics
Realistic Scale Simulation
pp collisions @ 14TeV minimum bias events produced by Pythia 8
2015 CMS detector
4T uniform magnetic field
  Decent approximation of the real solenoidal field
Low energy cut at 1MeV
‘Tabulated’ Physics
  Library of sampled interactions and tabulated x-sections
Same test (described above) run with both Geant4 and GeantV with various versions of the Geometry library.

## Slide 30: Checking basket overhead
CMS Yardstick
Comparison of
  Early GeantV scheduler w. TGeo (the geom package of ROOT) in single thread
  Geant4
Not a strict performance comparison
But a circumstantial proof that the overhead of basket handling is under control
We still had to work on multithreading scalability
CMS Ecal

## Slide 31: Architectural options
Baskets can contain SOA “contiguous” tracks
  Pro: data contiguity necessary for SIMD is maintained throughout
  Con: shuffling data implies copying
  Con: too much data is served both to physics and to geometry
Baskets can contain pointers to AOS tracks
  Pro: shuffling is just moving pointers
  Pro: only the necessary data is served to each subsystem
  Con: gather-scatter is necessary
The first option is the baseline
We are evaluating now the second option

## Slide 32: Basketizer performance
Investigated different ways of scheduling & sharing work - lock free queues, ..
  Changes in scheduler require non-trivial effort (rewrite)
Amdahl law effect still large, due to high re-basketizing load (concurrent copying)
  O(105) baskets/second on Intel Core i7™
  Algorithm already lock free
  Rate will go down with physics processes
Ongoing work to improve scalability
  Re-use baskets in the same thread after step if enough particles doing physics-limited steps
  Clone scheduling in NUMA aware groups, important for many cores (e.g. KNL)
Lock-free algorithm
(memory polling)
Algorithm using spinlocks
Rebasketizing
2x Intel(R) Xeon(R) CPU E5-2630 v3 @ 2.40GHz
RAM_1
RAM_2
GeantPropagator (NUMA manager)
Scheduler1
Scheduler2
Transport
queue1
queue2
Work stealing only
when needed
CPU1
CPU2
MPI manager

## Slide 33: Status on GPU
Broker adapts baskets to the coprocessor
  Selects tracks that are efficiently processed on coprocessor
  Gather in chunk large enough (e.g. 4096 tracks on NVidia K20)
  Transfer data to and from coprocessor
  Execute kernels
On NVidia GPU, we are effectively using implicit vectorization
  Rather than one thread per basket (on GPUs) we use 4096 threads each processing one of the tracks in the basket
Cost of data transfer is mitigated by overlapping kernel execution and data transfer
  We can send fractions of the full GPU's work asynchronously using streams

## Slide 34: Geometry - VecGeom
Geometry takes 30-40% CPU time of typical Geant4 HEP Simulation
A library of vectorised geometry algorithms to take maximum advantage of SIMD architectures
Substantial performance gains also in scalar mode
Better scalar
code

## Slide 35: Evolution
VecGeom code has been developed for GeantV vectorised transport
USolids was developed to unify TGeo and Geant4 geometry packages
Now VecGeom algorithms are retrofitted to USolids and are available both to Geant4 and to TGeo
VecGeom has the potential to introduce a %-level gain for Geant4 (to be verified)
  Algorithm improvement and (internal) vectorisation of some shapes
VecGeom is the consolidation both on the algorithm level and on the developer level of G4-Geo, TGeo, USolid and Vectorization efforts.
One becomes two, two becomes three, and out of the third comes the one as the fourth. Maria Prophetissa (3rd century AD)

## Slide 36: Geometry in HEP simulations
36
Detector description
  Hierarchical, multi-level structure of 'mother' and 'daughter' shapes
  Allow for the replication of common composite elements
Class concepts for separate responsibilities:
  Geometrical properties: shapes, dimensions
  Geometrical algorithms: containment, distances, volumes, normal vectors, Extent, etc.
  Relative positioning, coordinate transformations, materials
Navigation
  Given track parameters: position (x,y,z) and direction (px,py,pz), predict particle trajectories and intersections with any geometrical boundaries.
  External managers will take care of interactions with physics processes (including magnetic fields) and updates to track properties and positioning, display, etc.
Notes: 2/16/16
36
36

## Slide 37: Specialized Library.
Backward compatibility with ROOT and Geant4
Continue the already started AIDA USolids project
Numerical simulation have special requirements on numerical stability (double vs float, no leaks, we transport things across boundaries often not the case in 3D graphics engines)
HEP use specialized volumes not existing in external packages (polycone) and we can put a lot of domain specific knowledge to accelerate things
Single solution for CPU and GPU
Rely on special functions "safety" which might not exist in classical 3D rendering engines (which concentrate on hit detection)
Need an exact volume representation (and not a triangle approximation).
Different scale than most 3D graphics engines (that often have far fewer things to treat)

## Slide 38: Portability
Long-term maintainability of the code
  write one single version of each algorithm and to specialise it to the platform via template programming and low level optimised libraries (Vc in our case)
A Xeon Phi specific backend is being developed in collaboration with CERN’s openlab (UME::SIMD)
Results are quite encouraging: maybe portable HPC is NOT an oxymoron after all…
http://code.compeng.uni-frankfurt.de/projects/vc
template<class Backend>
Backend::double_t
common_distance_function( Backend::double_t input )
{
// Algorithm using Backend types
}
struct VectorBackend
{
typedef Vc::double_v double_t;
typedef Vc::bool_v bool_t;
static const bool IsScalar=false;
static const bool IsSIMD=true;
};
1 particle API
Many particle API (SIMD)
Common C++ template functions
Vc::double_v distance( Vc::double_v );
double distance( double );
“Backend” is a (trait) struct encapsulating standard types/properties for “scalar, vector, CUDA” programming; makes information injection into template function easy
struct ScalarBackend
{
typedef double double_t;
typedef bool bool_t;
static const bool IsScalar=true;
static const bool IsSIMD=false;
};

## Slide 39: Avoiding code duplication
Support of multiple platforms usually means multiple versions of source code
What are the differences between the two versions of code shown on the right?
Primarily: types and their operators, function attributes (__device__), also some higher level functions, e.g. conditional assignment
Avoid code duplication by abstracting away differences into common types or overloaded functions defined in trait structures.
cuda
Vc
Notes: 2/16/16
39
39

## Slide 40: Using traits to avoid code duplication
Intensive kernels are developed in a generic way, using only trait-defined types and functions.
Architecture-specific traits are created as needed, to associate generic types and functions with their arch-specific types.
Appropriate backends are requested by #define
backend/vc/Backend.h
backend/cuda/Backend.h
Notes: 2/16/16
40
40

## Slide 41: A generic kernel
The Backend, as discussed
MaskedAssign( ) is an optimized if( ) replacement
Arithmetics just works!
Notes: 2/16/16
41
41

## Slide 42: Example: Polycone
Speedup factor 3.3x vs. Geant4, 7.6x vs. Root • for most performance critical methods, i.e.:
It is today possible to run Geant4 simulations with Usolids/VecGeom shapes replacing Geant4 shapes (seamless to user)
VecGeom/USolids library is now shipped as an independent external library since release 10.2 of Geant4
USolids source code repository: gitlab.cern.ch/VecGeom/VecGeom
VecGeom/USolids is developed as part of the EU AIDA-2020 initiative.

## Slide 43: Geometry performance (Phi vs Xeon)
Geometry is 30-40% of the total CPU time in Geant4
A library of vectorized geometry algorithms to take maximum advantage of SIMD architectures
Substantial performance gains also in scalar mode
Testing the same also on GPU
 | 16 particles | 1024 particles | SIMD max
Intel Ivy-Bridge (AVX) | ~2.8x | ~4x | 4x
Intel Haswell (AVX2) | ~3x | ~5x | 4x
Intel Xeon Phi (AVX-512) | ~4.1 | ~4.8 | 8x
Overall performance for a simplified detector vs. scalar ROOT/5.34.17
Vectorization performance for trapezoid shape navigation (Xeon®Phi® C0PRQ-7120 P)

## Slide 44: Geometry performance on K20
Speedup for different navigation methods of the box shape, normalized to scalar CPU
  Scalar (specialized/unspecialized)
  Vector
  GPU (Kepler K20)
  ROOT
Data transfer in/out is asynchronous
  Measured only the kernel performance, but providing constant throughput can hide transfer latency
The die can be saturated with both large track containers, running a single kernel, or with smaller containers dynamically scheduled.
Just a baseline proving we can run the same code on CPU/accelerators, to be optimized

## Slide 45: The X-Ray benchmark
The X-Ray benchmark tests geometry navigation in a real detector geometry
X-Ray scans a module with virtual rays in a grid corresponding to pixels on the final image
  Each ray is propagated from boundary to boundary
  Pixel gray level determined by number of crossings
A simple geometry example (concentric tubes) emulating a tracker detector used for Xeon©Phi benchmark
  To probe the vectorized geometry elements + global navigation as task
  OMP parallelism + “basket” model
OMP threads

## Slide 46: Scalability and throughput
Better behavior using OMP balanced
  Approaching well the ideal curve up to native cores count
  Balanced threading converges towards the compact model as all the thread slots are filled
It’s worth to run Xeon Phi saturated for our application
The throughput performance for a saturated KNC is equivalent (for this setup) to the dual Xeon E5-2650L@1.8GHz server which hosts the card.
Notes: The compact model means threads are allocated on the same physical core until saturation level (i.e. 4 threads/core on MIC)

## Slide 47: Vector performance
Gaining up to 4.5 from vectorization in basketized mode
  Approaching the ideal vectorization case (when no regrouping of vectors is needed)
Vector starvation starts when filling more thread slots than the core count
  Performance loss is not dramatic
  Better vectorization compared to the Sandy-Bridge host (expected)
Scalar case: Simple loop over pixels
Ideal vectorization case: Fill vectors with N times the same X-ray
Realistic (basket) case: Group baskets per geometry volume

## Slide 48: Results on the Xeon Phi
Ideal parallelism for the code “hotspot”
Vectorisation intensity in excess of 10 for the most computationally demanding portions of the code

## Slide 49: What about physics?
Needed a “reasonable” shower development
Developed a library of sampled interactions and tabulated x-sections for GeantV
  Back ported to Geant4 for verification and comparison
A quick tool for developing realistic showers
  Potentially for developing into a fast simulation tool

## Slide 50: G4 example N03 vs tabulation (simple calo with many slabs)
profile
histos
FTFP-BERT

## Slide 51: What about physics?
Physics vectorisation has started with the electromagnetic processes
Compton scattering
  First vectorized process
  Shows good performance gains
Vector code is better scalar code!
We will validate & introduce this into Geant4
t(G4)/t

## Slide 52: Physics Performance
Objective: a vector/accelerator friendly re-write of physics code
Started with the electromagnetic processes
The vectorised Compton scattering shows good performance gains
Current prototype able to run an exercise at the scale of an LHC experiment (CMS)
  Simplified (tabulated) physics but full geometry, RK propagator in field
  Very preliminary results needing validation, but hinting to performance improvements of factors
Chart: Speed-up on Xeon Phi(R) C0PRQ-7120 for Compton KN model compared to Geant4
| 10.0 | 100.0 | 500.0 | 1000.0 | 5000.0 | 10000.0
T(Geant4)/T(Scalar) | 1.0843 | 1.125 | 1.1688 | 1.1818 | 1.1589 | 1.1686
T(Geant4)/T(Vector) | 5.7692 | 6 | 6.9231 | 6.0667 | 6.5177 | 6.6093
CMS Ecal

## Slide 53: GeantV Input
Input are the particles to be transported through the detector
  Collision events produced by generators (Pythia8, Herwig++, etc)
  Single “beam” particles for particular studies
Generic interfaces decouples generation and transport
Simulation threads concurrently process particles from the input
HepMC3 events file
HepMC3 event record (in memory)
GeantV detector simulation
reading
0.6ms / 14TeV min-bias pp event (negligible compared to simulation step)
Particles fed into concurrent simulation threads

## Slide 54: GeantV Output
Physics simulation produces ‘hits’ i.e. energy depositions in the sensitive parts of the detector
Those hits are produced concurrently by all the simulation (TransportTracks) threads
Thread-safe queues have been implemented to handle asynchronous generation of hits by several threads
Dedicated Output thread transfers the data from the output queues to ROOT I/O

## Slide 55: Hits/digits I/O
“Data” mode
  Send concurrently data to one thread dealing with full I/O
Chart: GeantV concurrent I/O 8 data producer threads + 1 I/O thread
| 0.71 | 2.95 | 4.78 | 8.07 | 13.61 | 19.88 | 22.69 | 22.8 | 22.99
Data I/O (old) | 0.066 | 0.074 | 0.07 | 0.057 | 0.114 | 0.379 | 1.51 | 2.5 | 3.41
Buffer I/O (new) | 0.053321 | 0.078998 | 0.16942 | 0.13351 | 0.33622 | 0.35752 | 0.66003 | 1.1679
“Buffer” mode
  Send concurrently local trees connected to memory files produced by workers to one thread dealing with merging/write to disk
Integrating user code with a highly concurrent framework should not spoil performance

## Slide 56: I/O On HPC
Challenges:
Individual output inherently has variable size (different number of particles, vertices, etc.)
Variability furthered by compression
Preparing data for output is CPU intensive
In practice can not do parallel write to the same file
Usual solution does not scale to HPC
  i.e. write one file per process.
Solution being explored:
Extend “Buffer” mode to multiple nodes
Set up a tree of nodes sending upstream the prepared output
Sending data in chunk during processing to maximize parallelism
Only a few end nodes processes or threads actually write to disks
  Cardinality close to the number of physical disk

## Slide 57: Putting It All Together - CMS Yardstick
Scheduler | Geometry | Physics | Magnetic Field Stepper
Geant4 only | Legacy G4 | Various Physics Lists | Various RK implementations
Geant4 or GeantV | VecGeom 2016 scalar | Tabulated Physics Scalar Physics Code | Helix Cash-Karp Runge-Kutta
GeantV only | VecGeom 2015 VecGeom 2016 vector Legacy TGeo | Vector Physics Code | Vectorized RK Implementation
Semantic changes

## Slide 58: Putting It All Together - CMS Yardstick
Scheduler | Geometry | Physics | Magnetic Field Stepper
Geant4 only | Legacy G4 | Various Physics Lists | Various RK implementations
Geant4 or GeantV | VecGeom 2016 scalar | Tabulated Physics Scalar Physics Code | Helix (Fixed Field) Cash-Karp Runge-Kutta
GeantV only | VecGeom 2015 VecGeom 2016 vector Legacy TGeo | Vector Physics Code | Vectorized RK Implementation
Semantic changes
1
2
3

## Slide 59: Putting It All Together - CMS Yardstick
Some of the improvements can be back ported to G4
Overhead of basket handling is under control
Ready to take advantage of vectorization throughout.
Improvement Factors (total) with respect to G4
Legacy (TGeo) Geometry library:
  1.5  Algorithmic improvements in infrastructure.
2015 VecGeom (estimate)
  2.4  Algorithmic improvements in Geometry
Upcoming VecGeom (early result)
  3.3  Further Geometric algorithmic improvements and some vectorization

## Slide 60: Next steps
Repeat the test with the introduction of
  Voxelisation in VecGeom
  Vectorised EM physics
  Vectorised transport in Mag Field
Develop simple classes for materials and particles to be able to run on coprocessors to enable physics on the GPU and Xeon Phi full CMS yardstick
… implementing a “preliminary performance yard-stick” combining all prototype features
  SIMD gains in the full CMS experiment setup
  Coprocessor broker in action: part of the full transport kernel running on Xeon®Phi® and GPGPU
  Scalability and NUMA awareness for rebasketizing procedure
  … achieving these just moves the target a bit further
… testing scaling up to large node count through MPI, e.g. on CORI
  Input distribution and Output gathering.

## Slide 61: Restating our case
We developed the three main components
  A multithread scheduler to handle the particle baskets
  A vectorised geometry library and navigator
  A vectorised Compton scattering and a tabulated physics list
Our results indicate that
  Basket handling introduces a minimal overhead
  SIMD gains half an order of magnitude in performance
An optimistic prediction based on our results gives an improvement factor beyond the 3.3 currently achieved on CPU
GPU and Xeon Phi improvement factors are expected to be higher
We are on track with achieving our objectives (see slide 22, 2 to 5 speedup)

## Slide 62: MiniApps - Try It Today
CMS Yardstick
  Full scale simulation of the CMS dectector
  MPI version available soon
XRayBenchMark
  Benchmark complete geometry modeler: shapes + navigation Developed X-Ray benchmark: propagate geantinos pixel-by-pixel
NavigationBenchmark
Can be run on CORI, See https://web.fnal.gov/project/Geant4RD/SitePages/Home.aspx
cd your_work_dir . ~pcanal/build_from_scratch # To run without rebuild use ~pcanal/geant_env.sh cd $BUILD_DIR/geant root.exe -b -l –q $SRC_DIR/geant/vecprot_v2/runCMS.C $BUILD_DIR/VecGeom/XRayBenchmarkFromROOTFile $SRC_DIR/geant/cmstrack/cms2015.root HB x 100 $BUILD_DIR/VecGeom/NavigationBenchmark -geometry $SRC_DIR/geant/cmstrack/cms2015 -logVol CALO

## Slide 63: Thank you!

## Slide 64: BACKUPS

## Slide 65: Explicit vectorization
Explicit SIMD vectorization can be implemented directly using intrinsics, but a vectorization library already brings many utilities pre-defined, like common math operators and functions.
VecGeom currently works with Vc library, by Mathias Kretz, but other libraries can be easily plugged in (Agner Fog's VCL, Intel's VML, Cilk Plus, …). A new backend is maybe all that is needed.
Notes: 2/16/16
65
65

## Slide 66: Data types supported
    Masks are not a feature, they are basic entity!
    From user perspective, mask is a set of boolean values.
    Swizzle masks (permute masks) are necessary for a large class of algorithms
    Swizzle mask is a set of indices representing a target order of elements in output vector.
UME::SIMD

## Slide 67: Data types supported
    Arithmetic vector types are what we are really interested in!
    Developers need to use vectors of arbitrary length
            Complex from from the code generation point of view
        Current interface defines vectors of lengths from 8-bit (SIMD1 x 8b int) to 1024 bit (SIMD128 x 8b int, SIMD16 x 64b double).
    The ability to use vectors of arbitrary length (e.g. based on UME::SIMD) will simplify the expression of algorithms
UME::SIMD
https://bitbucket.org/edanor/umesimd

## Slide 68: Physics developments: Multiple Scattering
G4 precision
G4 fast
GV
Sandia data
Source: M.Novak

## Slide 69: GeantV Multiple Scateeting
The new algorithm is being now vectorised for GeantV
It is in an experimental physics list for Geant4
  Candidate to become the default
Physics validation
Up to 30% faster in scalar
Less charged steps (30%-50%)

## Slide 70: Redesigning simulation: Physics interfaces
Maintain minimal coupling between kernel and physics
  Keep transportation in the kernel, outside the physics
Re-use as much as possible the design of Geant4 physics
  Avoid reinventing the wheel
Streamlining by reducing the inheritance depth
  Replace whenever possible, virtual polymorphism with static (template) polymorphism
  Offer thin interfaces for direct calls to cross sections and final-state models
Start with scalar signature (single-track) but keep in mind extension to track vectors

## Slide 71: Accelerators: plans for 2016
Porting and optimizing GeantV on BDW & KNL architectures
  Porting the prototype & adjusting programming model
  Profiling and understanding hotspots, reiterating first phase
  Tuning application parameters to optimize event throughput
Running the full prototype using GPU as co-processor
  Debugging the coprocessor broker and data flow through GPU
  Understanding performance issues and latency limitations
  Optimizing the application for the GPU cooperative mode (tuning scheduling parameters)